## Slide 1: Dataglove
Real time object classification by grasping via sensorized glove

## Slide 2: VMG30
Finger flex sensors (10) Measure the bending angle of each phalanx
Abduction sensors (4) Measure the angular distance between adjacent fingers
Pressure Sensors (5) Detect the force applied with the fingertips
Structural Sensors (2) Measure the overall posture of the hand
IMU Units (2) Provide 3D spatial orientation

## Slide 3: ROS2 architecture
Glove node
  Launches two parallel threads:
    Thread 1: reads data from the serial port
    Thread 2: publishes data on the /sensor topic
  Operating frequency: 100 Hz for both threads
Real time classifier node
  Subscribes to the /sensor
  Maintains a rolling window of 300 time samples
  Uses the buffered data to classify the object held by the glove in real time

## Slide 4: ROS2 architecture
Data saver node
  Subscribes to the /sensor
  Store to a file the received data
  Used for creating the dataset
Glove emu node
  Read data from a file
  Publish data to /sensor with a frequency of 100Hz
  Used to emulate the glove

## Slide 5: Dataset
6 object
  No object (rest position)
  Bottle
  Pen
  Phone
  Computer mouse
  Glasses case
Execute glove node and data saver node:
  ~ 1 second in rest position
  Move and grasp object
  ~ 1 second stationary with object in hand

## Slide 6: CNN-BiLSTM model with attention mechanism
2 convolutional layer
  Kernel size 1x3
2 Bi-LSTM layer
1 Attention Layer
2 Fully connected layer

## Slide 7: Bidirectional LSTM
LSTM are recurrent NN
They use gating mechanism to mitigate gradient vanishing problem
Bi-LSTM process input sequences in both forward and backward directions
This allows the model to capture context from both past and future states

## Slide 8: Attention mechanism
Score computation:
Attention weights:
Context vector:
A weighted sum of the scores produces the final context vector, which focuses on the most relevant parts of the input sequence.

## Slide 9: Model training
Dataset split:
60% – Training set
20% – Validation set
20% – Test set
Validation set used for:
Monitoring model performance during training
Implementing early stopping to avoid overfitting
Early stopping strategy:
Training is interrupted if no improvement in validation performance is seen for 50 consecutive epochs

## Slide 10: On test set
100% accuracy

## Slide 11: Demo Time

## Slide 12: Feature curve and most relevant sensor type
5-fold cross validation
  Points are the average value on validation sets
  Error bar are standard deviation on validation sets
Finger flex data are the most descriptive

## Slide 13: Continual learning
Class incremental learning: I want my classifier to be able to learn new classes (last two object)
Avoid retraining from scratch
Faster
Cheaper
Attention: Catastrophic forgetting

## Slide 14: Learning without forgetting
Save a copy of the old model – Teacher
Modify the FC layer of the model to add new classes and copy the shared weights – Student
Train only on new data:
  Task loss for the new classes - CE
  Distillation loss to retain knowledge of old classes - KL
Doesn’t require Buffer Replay

## Slide 15: LwF results
If 𝜆 is too large, the model focuses too much on preserving old knowledge
→ It fails to learn the new task properly
If 𝜆 is too small, the model prioritizes learning new data
→ It forgets the previous tasks
→ Catastrophic Forgetting
Choosing the right value of λ is essential to balance stability and plasticity but is hard

## Slide 16: Dark Experience Replay
Save a copy of the old trained model – Teacher
Modify the FC layer of the model to add new classes and copy the shared weights – Student
Accessing a small fraction of old data – Buffer Replay
Train at the same time on new and old data but using different loss
  Classification term + distillation term

## Slide 17: DER results
90% accuracy
New classes are learned successfully
Buffer replay is required but helps mitigate catastrophic forgetting
Easier to choose

## Slide 18: Conclusion
Implemented a state of the art neural network for classifying object via a sensorized glove
Implemented a ros2 program for real time classification
Compared two technique for continual learning:
Learning without forgetting
Dark experience replay

## Slide 19: Thanks for you attention. Bibliography:
Data glove-based gesture recognition using CNN-BiLSTM model with attention mechanism, Wu Jiawei et al. (journals.plos)
Learning without Forgetting, Zhizhong Li et al. (arXive)
Dark Experience for General Continual Learning: a Strong, Simple Baseline, Pietro Buzzega et al. (arXive)

## Slide 20: Without continual learning
97% accuracy
Class incremental learning worsen the overall performance of the model

## Slide 21: Feature curve and most relevant sensor type
5-fold cross validation
  Points are the average value on validation sets
  Error bar are standard deviation on validation sets
Finger flex data are the most descriptive